## Slide 1: SOLARSAFE – Dehumidification
James Edwicker, Zac Heggie, Josh Tuckwell

## Slide 2: Josh – Concept Design
The design goal is to increase the drying performance of the fan system.
Restrictions on:
  Power – Target of ~100W, with a strict maximum of 150W.
  Cost – Any increase must be proportional to performance gains and remain affordable for sub-Saharan Africa.
  Space and Mobility – The device must be portable to enable sharing between multiple farmers.

## Slide 3: Josh – Concept Design
Brainstormed methods to increase drying performance:
  Increase volumetric flow of air
  Increase air temperature passing over the maize
  Decrease inlet air humidity.
Found that increasing temperature by 1°C is equivalent to reducing humidity by 4%
Source: Penn State Extension, 2023.

## Slide 4: Josh – Dehumidification
Desiccant Dehumidification: Uses moisture-absorbing materials (like silica gel). Requires regular physical replacement or a high-temperature cycle to regenerate the material.
Vapour-Compression Refrigeration: Drops air temperature below its dew point to condense out water. Highly effective but bulky, power intensive, and structurally complex.
Thermoelectric / Peltier Cooling: Solid-state condensation that strips moisture from the inlet air. No moving parts or toxic refrigerants.

## Slide 5: Josh – Peltier Devices
(
Key Advantages | System Limitations (Design Constraints)
Ultra-Compact | Low Thermodynamic Efficiency (COP) compared to mechanical cycles.
High Reliability: No compressors, valves, or fluid | Extraction rates are typically <1 litre of water per day.
Low Cost & Quiet | Optimised for small spaces
Thermoelectric modules which actively transfer heat from one side of the ceramic substrate to the other using a DC current.
Creates a local cold sink to drop inlet air below its dew point, forcing moisture to condense.

## Slide 6: James – Rig Design
Motor & fan selection
Dehumidification parts
Ducting routing
Ducting cross-section
Water management
Air management

## Slide 7: James – Rig Design
Peltier
Humidity & Temp Sensors
Temp Element
Controller
Blower
180° Turn

## Slide 8: James – Risk Assessment and Parts Sourcing
Updating the risk assessment to meet departmental demands
Filtering material and parts options to find suitable purchases
Key issues:
  Motor & fan
  Ducts
  Peltier heat sinks

## Slide 9: Zac – Electronics Architecture

## Slide 10: Zac – Devices
Gravity: DHT11 Temperature & Humidity Sensor For Arduino
High Power Double DC Stepper Motor Driver Module Board H-Bridge PWM
SEAFLO IN LINE BLOWER 12V 4" MARINE BOAT VENTILATION in-line air vent inline

## Slide 11: Zac – Devices
Thermoelectric Cooler Cooling Peltier Plate Module 12V 6A
12V AC DC Universal Constant Temperature Air Heater

## Slide 12: Project Timeline Update